## Slide 1: BASIC CHEMICAL STRUCTURE, ATOMS, MOLECULES, IONS.
BY
DR M.K DOLA

## Slide 2: INTRODUCTION
Gasoline is an extremely flammable fuel source for automobiles which consists mainly of light hydrocarbons produced by refining crude petroleum . The most important property of gasoline which determines its quality is the octane number. Octane number is the measure of the anti-knock property of gasoline in spark-ignition engine.
Objective
  To obtain gasoline with high octane number from heavy diesel oil and vacuum gas oil.
  Increase the octane number of straight run gasoline, straight run naphtha and reformate by blending with Fluid catalytic cracking (FCC) gasoline.
Scope of work
  Focused on the Fluid catalytic cracking unit of a refining plant to enhance gasoline octane number

## Slide 3: LITERATURE REVIEW I
OCTANE NUMBER
  It is defined as the volume percent of i-octane in a blend of n-heptane and i-octane, which produces the same knock intensity as the test fuel under standard conditions in an American Society for Testing materials (ASTM) spark-ignition engine.
  Octane number is measured in two ways;
  Research Octane Number (RON)
  Motor Octane Number (MON)
KNOCKING IN SPARK-IGNITION ENGINES
  Knocking is an abnormality that occurs as a result of rapid combustion of an unburned fuel-air mixture in the front of the normal flame front. This is characterized by a certain percentage of iso-octane in a binary mixture of iso octane and n-heptane which constitutes the octane rating of a given gasoline.
  Gasoline is classified into two based on their octane rating;
  Regular Motor Spirit (RMS)
  Premium Motor Spirit (PMS)

## Slide 4: LITERATURE REVIEW II
ANTI-KNOCK AGENTS
  An anti-knock agent is a gasoline additive used to reduce engine knocking and increase the gasoline octane rating. Some typical anti-knock agents are;
  Tetra-ethyl lead (TEL) (phased out)
  Methylcyclopentadienyl manganese tricarbonyl (MMT)
  Ferrocene
  Iron pentacarbonyl
  Toluene
  Iso-octane
OXYGENATES
  An oxygenate is any fuel that contains oxygen. This increases the properties of gasoline such as fuel blend water tolerance, volatility characteristics as well as the octane rating.

## Slide 5: LITERATURE REVIEW III
CONVERSION PROCESSES
  These are chemical processes which are used to produce gasoline with high octane rating . They include;
  Catalytic Reforming
  Isomerization
  Alkylation
  Polymerization
  Hydrocracking
  Fluid Catalytic Cracking
Fluid Catalytic Cracking
  This is a chemical process used in the petroleum refinery to convert heavy molecular weight hydrocarbons such as heavy diesel oil (HDO) and heavy gas oil (VGO) to light molecular weight hydrocarbon which includes gasoline with high octane rating. It uses the zeolite catalyst which are of types;
  Type X zeolite
  Type Y zeolite
  ZSM-5
  USY zeolite

## Slide 6: METHODOLOGY I
Fluid catalytic cracking unit of Port Harcourt Refining Company is studied as one of the ways of producing gasoline with a high octane rating.
Vacuum gas oil (VGO) and heavy diesel oil (HDO) are the feed stock used to carry out the process.
  VGO feed stock properties HDO feed stock properties
VGO(crude source) | Bonny light
Feed flow rate (m3/H) | 160
Gravity, API | 21,2-22,9
Sulfur content, wt% | 0.19
Nitrogen content, wt% | 0.15
Kinematic viscosity, cst at 99*C | 8.8
Conradson carbon, wt% | 0.23
Metal content (Ni+V), wt. ppm | 0.085
IBP (oC) | 531
EP (oC) | 602
HDO feed stock (crude source) | Bonny light
Gravity, API | 26,5-30,0
Sulfur content, wt% | 0.18
Nitrogen content, wt% | 0.07
Conradson carbon, wt% | 0.01
Metal content (Ni+V), wt. ppm | 0.04
IBP (oC) | 369
EBP (oC) | 384

## Slide 7: METHODOLOGY II
PROCESS DESCRIPTION
Reactor/ Regenerator Section
Fractionation Section
Gas concentration Section
Flue Gas Cooler
Merox Unit (Gas treatment)
Flue gas to stack
Flue gas
Feed
MCB
LCO
LPG
Gasoline
Fuel Gas

## Slide 8: METHODOLOGY III
SAMPLE COLLECTION AND TESTING
  Gasoline sample is collected from the product sample point and taken to the process laboratory where the various properties are tested.
STANDARD TEST FOR GASOLINE OCTANE NUMBER USING COOPERATIVE FUEL RESEARCH ENGINES (CFR) (ASTM TESTS D2699 & D2700)
  The octane number is determined through a process of interpolation where the operation involves using two reference fuels (n-heptane and iso-octane). The sequence is low reference fuel, test sample, and high reference fuel where the knock meter reading is high of low octane fuel which indicates high knock intensity and low for high octane fuel which indicates low knock intensity.

## Slide 9: RESULT AND DISCUSSION I
LABORATORY RESULT
  Result from the process laboratory shows the properties of sample gasoline from FCC which include the octane number (RON and MON), Reid vapor pressure (RVP), distillation profile, sulfur content, specific gravity etc
Properties | Test methods | Gasoline Sample | FCC feed
Sp. G @ 15/15 oC | IROX test | 0.7677 | 0.9385
RVP kg/cm2 | ASTM D323 | 0.32 | 
IBP, oC | ASTM D86 | 45 | 271
EBP, oC | ASTM D86 | 204 | 602
Sulfur content ppm | ASTM D4294 | 0.04 | 0.19
MON | ASTM D2700 | 89.9 | 
RON | ASTM D2699 | 95.9 | 

## Slide 10: RESULT AND DISCUSSION II
EFFECT OF REACTOR TEMPERATURE ON OCTANE NUMBER
  With increase in the reactor temperature cracking becomes more severe thereby increasing the olefin and aromatic content of the product gasoline , hence increases the octane number.
Reaction Temp, oC | Olefins vol% | Aromatics vol% | Octane number (GC)
763 | 24 | 16 | 0
773 | 25 | 18 | +0.5
783 | 27 | 20 | +1.4
Chart: Relationship between Reactor temp. and olefin and aromatic content of gasoline
| 763 | 773 | 783
Olefin vol% | 24 | 25 | 26
Aromatics vol% | 16 | 18 | 20

## Slide 11: RESULT AND DISCUSSION III
PREPARED GASOLINE POOL
  Comparing FCC gasoline to the gasoline from other processes in the refinery, FCC gasoline stands out with a very high octane number. In other to upgrade the gasoline from other units, a gasoline pool is prepared where FCC gasoline is blended with gasoline from the other processes.
Component | RON | Volumetric flow rate (m3/hr) | Composition in gasoline pool (%) | Expected RON
FCC gasoline | 95.9 | 94.3 | 61.73 | 59.2
SRG | 71 | 7.2 | 4.72 | 3.4
SRN | 62 | 7.0 | 4.57 | 2.8
Reformate | 92 | 44.3 | 28.98 | 26.7
Total |  | 152.8 | 100 | 92.1

## Slide 12: RESULT AND DISCUSSION IV
Chart: Comparing FCC gasoline
| FCC gasoline | Reformate | SRG | SRN
Research Octane Numbers | 95.9 | 92 | 71 | 62
Chart: 
| FCC Gasoline | SRG | SRN | Reformate
Model of the Gasoline pool | 61.73 | 4.72 | 4.57 | 28.98

## Slide 13: RESULT AND DISCUSSION V
LABORATORY RESULT OF SAMPLE FROM GASOLINE POOL
  Through product blending, FCC gasoline and reformate which have a high octane rating are blended with SRG and SRN to increase the volume of the finished motor gasoline from the refinery while maintaining a high octane rating. The finished gasoline ready for shipping is in a premium grade, hence called premium motor spirit (PMS).
Properties | Gasoline pool sample
Specific Gravity | 0.7480
IBP oC | 31
EBPoC | 189
RVP kg/cm2 | 0.61
RON | 92.1

## Slide 14: CONCLUSION
Based on the results and previously discussed analyses, the following conclusions may be drawn;
Increase in the reaction temperature to 783k below the catalyst deactivation temperature makes the cracking more severe by increasing the aromatic and olefin content of gasoline thereby increasing the octane number of gasoline.
Fluid catalytic cracking produced gasoline with research octane number (RON) of 95.9
FCC gasoline and Reformate from catalytic reforming were blended with straight run gasoline (SRG) and straight run naphtha (SRN) to produce a gasoline pool called Premium motor spirit (PMS) with a research octane number (RON) of 92.1.

## Slide 15: RECOMMENDATION
Through the period of this study, the following recommendations can be made;
Options on zeolite catalyst should be investigated for low cost catalyst that would be resistant to thermal deactivation, have less metal poisoning, high attrition resistance, sintering index and most importantly high activity thereby increasing gasoline yield with a high octane.
Sulfur and nitrogen content of the feedstock should be minimal to avoid corrosion of equipment and to minimize the sulfur and nitrogen content in the product gasoline to avoid air pollution.
Metal content of the feed should be completely removed to avoid catalyst deactivation.

## Slide 16: THANK YOU.